## Slide 1
Physics-Informed Reconstruction of Cylinder Flow with Reynolds Continuation
PINN-based reconstruction and transition analysis for 2D incompressible flow past a cylinder
Junhe Chen
Spring 2026

## Slide 3
Project Overview
Physical problem, objectives, and expected transition behavior
Problem Statement
2D incompressible flow past a circular cylinder is a canonical benchmark in fluid dynamics.
As Reynolds number increases, the wake evolves from steady symmetric recirculation to time-periodic vortex shedding.
This project uses a Physics-Informed Neural Network (PINN) to reconstruct the flow field and study the transition region.
Geometry and setup
Cylinder radius R = 0.5
Domain x in [-5, 25], y in [-10, 10]
Target Reynolds sweep: Re = 5 to 100
Main Deliverables
Flow reconstruction
Velocity, pressure, vorticity, and streamlines
Reusable pipeline
Continuation training across Reynolds numbers

## Slide 4
Governing Equations and PINN Formulation
2D incompressible Navier-Stokes with stream-function parameterization
Navier-Stokes Equations
u_t + u u_x + v u_y = -p_x + (1/Re)(u_xx + u_yy)
v_t + u v_x + v v_y = -p_y + (1/Re)(v_xx + v_yy)
u_x + v_y = 0
The PINN minimizes PDE residuals together with boundary, initial, and outlet constraints using automatic differentiation.
Stream Function Form
Represent the solution as
psi(x, y, t), p(x, y, t)
u = d psi / d y
v = - d psi / d x
Enforces incompressibility by construction.
Removes the need for an extra divergence penalty term.
Produces smooth derivatives compatible with PDE residual evaluation.

## Slide 5
Network Architecture, Training, and Loss Design
Model Architecture
(x, y, t) --> MLP --> (psi, p)
Width
128 neurons/layer
Depth
6 hidden layers
Activation
tanh
Optimizer
Adam + L-BFGS
Loss Function
L = L_pde + 10 L_bc + 10 L_ic + L_out
PDE loss: momentum residuals from Navier-Stokes.
Boundary loss: inlet, wall, and far-field conditions.
Initial loss: uniform initialization in the domain.
Outlet loss: pressure / gradient regularization downstream.
Sampling Strategy
Physics-aware collocation
50%
30%
20%
Refine points near the cylinder to capture boundary-layer behavior.
Bias sampling in the wake to resolve separation and shedding.
Use smoother activation and derivatives for stable AD-based training.

## Slide 6
Reynolds Continuation Strategy
Warm-starting across Reynolds numbers to improve optimization stability
Continuation Workflow
Re = 5
Initialize low-Re steady solution
Re = 40
Transfer weights and continue training
Re = 40-60
Resolve transition region carefully
Re = 61-100
Track increasingly unsteady wake dynamics
More stable optimization
Fewer iterations at each new Re
Better continuity across the parameter sweep

## Slide 7
Results Placeholder: Flow Reconstruction
Replace placeholder panels with your exported figures
Key observations
Velocity magnitude should show stagnation at the front face and acceleration near the cylinder sides.
Downstream recovery and recirculation bubble length can be compared across Reynolds numbers.
Use the same colorbar range when comparing multiple Re values.
Recommended figures
• Velocity magnitude contour at representative times
• Streamline plot showing wake topology
• Optional comparison: Re = 40, 60, 100

## Slide 13
Results Placeholder: Vorticity and Probe Signals
Use these for wake structure and time-series evidence of transition

## Slide 15
Run A — Sanity Configuration and Commands
Re=40 single-snapshot PINN, baseline domain and point counts
SLURM allocation + training command
# 1) interactive GPU node
salloc -p gpu --gres=gpu:1 \
--mem=128G -t 12:00:00
# 2) Run A baseline training
python -u cfp40.py --vtk-path Re40.vtk \
--save-dir checkpoints_sanity_A \
--viz-dir viz_sanity_A \
--width 96 --depth 5 \
--epochs-adam 1500 \
--maxiter-bfgs 500 --iters-per-batch 100 \
--n-f 20000 --n-data 8000 \
--n-cfd-pde 4000 --lambda-pde-cfd 2.0 \
--cfd-pde-wall-buffer 0.5 \
--cfd-pde-edge-buffer 0.5 \
--x-min -3 --x-max 12 \
--y-min -4 --y-max 4 \
--method-bfgs SSBroyden1
Why these knobs (vs. previous run)
Custom BFGS path fixed
Now actually invokes SSBroyden1 from
_optimize._minimize_bfgs. Old code passed
method_bfgs=… into scipy stock BFGS where
it was silently dropped → standard BFGS.
Frozen colloc + full data in BFGS
BFGS gets a deterministic objective; data
MSE can monotonically decrease.
CFD-PDE buffer = 0.5
Skips boundary-layer / far-field CFD
points where the CFD itself violates NS
(see CFD-PDE residual slide).
Memory budget check enabled
Aborts before Adam if H0 (NxN float64)
won't fit. 96/5: H0 ≈ 11 GB.
Junhe Chen | PINN Cylinder Flow Reconstruction
Brown University
8

## Slide 16
Run A — Loss Trajectory and Achieved Error
Adam (1500 ep) → SSBroyden1 (500 calls); training-DATA dropped 30×, but full-mesh MAE much higher
Numbers (analysis_runA/summary.txt)
Training-time data MSE
plateau ≈ 2.4·10⁻⁴
(sampled, wake-biased)
Full-mesh MAE (4869 pts)
mae_u = 1.247·10⁻¹
mae_v = 6.77·10⁻²
rel_l2_uv = 0.238
Surprise:
training-DATA suggested
MAE ~ 1.5·10⁻²; actual
MAE is ~10× larger. Wake-
biased sampling masked
inlet/far-field error.
L_wall_uv ≈ 3·10⁻¹⁵
(machine ε² — see slide 10)
PDE rmse mag = 0.366
near_cyl ÷ far ≈ 15×
Lesson: judge progress by full-mesh MAE, not training-DATA. Random training samples are biased toward the wake (wake_frac=0.8).
Junhe Chen | PINN Cylinder Flow Reconstruction
Brown University
9

## Slide 17
Hard No-Slip via Stream-Function Lifting
Why L_wall_uv saturates at machine ε² ≈ 10⁻¹⁵ instead of being optimised
From the lift conditions to ⟨u² + v²⟩ ≈ ε²
Define r(x,y) = √((x−x_c)² + (y−y_c)²), ψ = lift(r) · ψ_raw → ∇ψ = lift′(r)·r̂·ψ_raw + lift(r)·∇ψ_raw
lift(R) = tanh²(0) = 0, lift′(R) = 2 tanh(0) sech²(0) / δ = 0 ⇒ ∇ψ|_{r=R} = 0 ⇒ u = ∂_y ψ ≡ 0, v = −∂_x ψ ≡ 0 on the wall.
Numerically: fp32 unit round-off ε ≈ 6·10⁻⁸ on each velocity ⇒ L_wall_uv = ⟨u² + v²⟩ ~ ε² ≈ 4·10⁻¹⁵. Run-A measured max|u|=2.0·10⁻⁷ ✓
Junhe Chen | PINN Cylinder Flow Reconstruction
Brown University
10

## Slide 18
Is the CFD itself a solution of the PDE?
Steady vorticity-transport residual on the Re40 mesh — sets the achievable PINN floor
Method
On every interior CFD point:
(1) k-nearest neighbours,
(2) local quadratic fit to u and v,
(3) read u_x, u_y, ..., v_xy at center,
(4) ω = v_x − u_y,
(5) second fit for ω → ω_x, ω_y, ω_xx, ω_yy,
(6) compute r_ω = u·ω_x + v·ω_y
− (1/Re)(ω_xx + ω_yy).
Curl of momentum eliminates pressure
→ no need to know p from the VTK.
Three configurations tested:
• k=24, buf=0.15 (default)
• k=12, buf=0.15 (tighter neighbour fit)
• k=24, buf=0.5 (exclude BL + edge band)
Take-away: bulk CFD median NS residual ≈ 1·10⁻³ → 1e-4 ~ 1e-5 absolute MAE is NOT achievable while also satisfying the PDE on this mesh.
Junhe Chen | PINN Cylinder Flow Reconstruction
Brown University
11

## Slide 19
Run A — Velocity Agreement on CFD Points
Per-component scatter and absolute error map (4869 points, full PDE box)
Measured numbers
mae_u
1.247·10⁻¹
mae_v
6.77·10⁻²
rel_l2_uv
0.238
rel_l2_v large because
|v_true| is small here;
look at mae_v not rel.
Spatial pattern:
error concentrates
near cylinder + wake
shear layer; smooth
decay in far field.
Junhe Chen | PINN Cylinder Flow Reconstruction
Brown University
12

## Slide 20
Run A — PDE Residual on Collocation Points
Where the trained PINN still violates Navier–Stokes
Compatibility
pde_rmse_mag
3.66·10⁻¹
near_cyl_pde_rmse_mag
8.53·10⁻¹ (×15 of far)
far_pde_rmse_mag
5.75·10⁻²
pde_p99_mag
2.00·10⁰
Reading the map:
bright ring at r≈0.5–1.5
⇒ unresolved boundary
layer; same place where
CFD also fails NS
(slide 11 / diagnostic).
Junhe Chen | PINN Cylinder Flow Reconstruction
Brown University
13

## Slide 21
Run A — Boundary-Condition Diagnostics
Wall (hard-enforced) vs inlet / top / bottom (soft penalties)
Wall: max|u|=2.0·10⁻⁷, max|v|=1.4·10⁻⁷ (fp32 ε ≈ 6·10⁻⁸ → matches lift-derivation, slide 10). Inlet rmse(u−1)=0.20, top/bottom 0.17/0.15 ← soft BC weights too low; PINN traded them off vs data.
Junhe Chen | PINN Cylinder Flow Reconstruction
Brown University
14

## Slide 22
Run A — Vorticity: PINN vs CFD
Derivative-level comparison (harder than velocity-level fit)
Numbers and reading
vort_rmse
2.71
vort_max_abs
7.86 (CFD peaks at 8.1)
PINN range: [-4.3, +8.4]
CFD range: [-8.1, +8.1]
PINN under-resolves the
negative shear lobe.
Junhe Chen | PINN Cylinder Flow Reconstruction
Brown University
15

## Slide 23
Run A vs Run B — Effect of 4× Collocation Points
Mentor's first hypothesis: more colloc points → lower loss. Tested as a controlled A/B.
Setup
Run A Run B
n_f 20 000 80 000
n_cfd_pde 4 000 16 000
n_data 8 000 8 000
Adam ep. 1 500 1 500
BFGS calls 500 500
network 96/5 96/5
Result
Training-DATA plateau:
Run A: 2.32·10⁻⁴
Run B: 1.46·10⁻⁴ (1.6×↓)
Run A full-mesh eval (4869 pts):
mae_u = 0.125, mae_v = 0.068
rel_l2_uv = 0.238
Run B mae (sqrt-ratio est.):
mae_u ≈ 0.099, mae_v ≈ 0.054
4× more colloc points → 1.6× lower training-DATA plateau (2.32→1.46·10⁻⁴); estimated mae improvement ≈ 21% (sqrt of ratio).
Eval MAE 0.125 ~ 8× larger than √(training-DATA) = 0.015 — wake-biased sampling masks inlet / far-field error. Judge by full-mesh eval, not training log.
1e-4 absolute MAE remains unreachable while respecting PDE — CFD's own NS residual median ≈ 1·10⁻³ (slide 11).
Junhe Chen | PINN Cylinder Flow Reconstruction
Brown University
16

## Slide 24
v2 Experiments At a Glance
All Re=40 runs since the Run A/B baseline (slide 23); same vtk reference, same domain (-8,12)×(-8,8)
setup | net | data anchor | PDE | mae_u | mae/P1 | PDE drop
A1+A2 two-stage (early v2 win) | 96 / 5 | 10k pts, prio=5 → 0 | 20k | 0.047 | — | —
P1 baseline (data-only, all CFD) | 32 / 3 | all CFD pts | off | 0.106 | 1.00× | —
strict consistency (P2, no data) | 32 / 3 | OFF | 20k | 0.339 | 3.20× | huge (→0)
weak anchor (P2, 500 pts) | 32 / 3 | 500 pts, prio=0.5 | 20k | 0.174 | 1.64× | —
all-CFD anchor (P2, prio=0.5) | 32 / 3 | all CFD pts | 20k | 0.157 | 1.48× | 1.57×
all-CFD anchor (P2, prio=1.0) | 32 / 3 | all CFD pts | 20k | 0.141 | 1.33× | 1.45×
all-CFD anchor (P2, prio=2.0) | 32 / 3 | all CFD pts | 20k | 0.128 | 1.21× | 1.17×
all-CFD anchor (P2, prio=5.0) | 32 / 3 | all CFD pts | 20k | 0.118 | 1.11× | 0.95×
scale-up (P2, prio=2.0) | 64 / 4 | all CFD pts | 20k | 0.021 | 1.15× | 5.97×
Only the scale-up row clears both columns. All-CFD-anchor at the small net keeps the field within ~1.5× P1 but PDE barely drops; removing data (red row) lets PDE drop hard but the field collapses 3.2×.
Junhe Chen | PINN Cylinder Flow Reconstruction | Brown University
24

## Slide 25
Strict Consistency (P2 with no data) — Trivial Attractor
width=32, depth=3. Phase 1 = data only; Phase 2 = PDE only (n_f=20k).
P1 mae_u (data-only)
0.106
baseline
P2 mae_u (no data)
0.339
3.2× drift
PDE residual
→ 0
meets weak (X)
Wake recirculation
lost
fails strict (Y)
Without a data anchor, BFGS finds a different minimum of the PDE objective — one that drives ‖f_NS‖ → 0 but no longer matches the CFD wake. The field relaxes toward (u,v) ≈ (1,0) in most of the domain.
This is the trivial-attractor mode: uniform free-stream satisfies incompressible Navier–Stokes everywhere except a thin wall layer. Hard BCs make it accessible but do not exclude it.
Junhe Chen | PINN Cylinder Flow Reconstruction | Brown University
25

## Slide 26
data_priority Sweep with Full CFD Anchor — Monotonic Trade-off
Same small net (32/3). Phase 2 keeps all 7456 CFD pts on, only the anchor weight changes.
data_priority | mae_u | mae/P1 | PDE start → end | PDE drop
0.5 | 0.157 | 1.48× | 0.652 → 0.416 | 1.57×
1.0 | 0.141 | 1.33× | 0.653 → 0.451 | 1.45×
2.0 | 0.128 | 1.21× | 0.545 → 0.467 | 1.17×
5.0 | 0.118 | 1.11× | 0.549 → 0.581 | 0.95× (up)
What the sweep says
priority ↑ ⇒ mae drift ↓ but PDE drop ↓.
Strict monotonic trade-off — no sweet spot meets both halves of (Y) at this capacity.
Best mae (1.11×) and best PDE drop (1.57×) sit at opposite ends of the curve.
Interpretation
At width=32, depth=3 the CFD-matching minimum and the low-PDE-residual minimum live on different sheets of parameter space.
Tuning the anchor only slides the optimiser along the trade-off curve — it cannot make the two minima merge.
Junhe Chen | PINN Cylinder Flow Reconstruction | Brown University
26

## Slide 27
Scale-Up — Achieved by Capacity, Same Protocol
Only width and depth changed. data_priority=2 fixed; all CFD pts kept on; n_f=20k.
P1 mae_u (big net)
0.0186
5.7× better than small (0.106)
P2 mae_u
0.0213
rel_l2_u = 0.032
mae P2/P1
1.15×
(Y) needs ≤ 2× ✓
PDE 0.084 → 0.014
5.97×
(Y) needs ≥ 5× ✓
 | width / depth | params | P1 mae_u | P2 mae_u | mae/P1 | PDE drop
small (32 / 3) | 32 / 3 | ~3k | 0.106 | 0.128 | 1.21× | 1.17×
scale-up (64 / 4) | 64 / 4 | ~17k | 0.0186 | 0.0213 | 1.15× | 5.97×
Conclusion
At width=64 the CFD-matching minimum and the low-PDE-residual minimum are essentially the same point. Both halves of (Y) are met simultaneously with the same Phase-1 / Phase-2 protocol and the same data_priority=2.
Junhe Chen | PINN Cylinder Flow Reconstruction | Brown University
27